## Slide 1: DDCA Project
Gray Code to Binary Converter
1
0
0
1
TEAM MEMBERS
PARVATHANENI PAVAN VIRESH CHOWDARY
2620040035
PENDLI SLESHA REDDY
2620040036
JALADI ROHITA
2620040040
VEERNALA SAI RAM VENKATA SATHWIK
2620040073
KLH University, Bachupally, Hyderabad

## Slide 2: Problem Statement
OBJECTIVE
Design a Gray code to binary converter and explain its working and applications.
1
Understand
Learn how Gray code changes only one bit per step
2
Design
Derive logic equations and build it with XOR gates
3
Apply
Verify with a truth table and real-world uses

## Slide 3: What is Gray Code?
A binary system where consecutive values differ in only one bit
Also known as reflected binary code
Prevents errors when many bits would change at once
1 bit
changes between every two consecutive codes
Decimal | Binary | Gray
0 | 000 | 000
1 | 001 | 001
2 | 010 | 011
3 | 011 | 010
4 | 100 | 110
5 | 101 | 111
6 | 110 | 101
7 | 111 | 100

## Slide 4: Working: Gray to Binary
The MSB stays the same. Each next binary bit is the previous binary bit XOR the current Gray bit.
B3 = G3
B2 = B3 ⊕ G2
B1 = B2 ⊕ G1
B0 = B1 ⊕ G0
⊕ is XOR: the output is 1 only when the two inputs differ.
WORKED EXAMPLE
Gray code: 1101
B3 = 1
B2 = 1 ⊕ 1 = 0
B1 = 0 ⊕ 0 = 0
B0 = 0 ⊕ 1 = 1
Binary: 1001

## Slide 5: Circuit Design (4-bit)
G3
B3
G2
B2
XOR
G1
B1
XOR
G0
B0
XOR
Gray code input
XOR gate
Binary output
Only 3 XOR gates are needed for 4 bits. Each output feeds the next gate.

## Slide 8: Applications
1
Rotary Encoders
Position sensing with no false readings
2
Analog-to-Digital
Safer code transitions in converters
3
Asynchronous FIFOs
Pointers cross clock domains safely
4
K-Map Design
Gray order simplifies logic minimization
5
Low-Power Counters
One bit flips per count, less switching
6
Robotics and Sensors
Reliable angle and position feedback

## Slide 9: Thank You
1
0
0
1
Gray Code to Binary Converter | DDCA Project